## Slide 1
CSA07 — COMPUTER NETWORKS
OSI Layer Concept Mapping
Six questions — six new structures: timeline, card-stack, ladder, swimlane, loop, checklist
SIMATS Engineering | Assessment Tool 2 | Annexure A

## Slide 2
Question 1
Completing the Concept Map of OSI Layers
Application → Presentation → ______ → Transport → Network → ______ → Physical. Structure: horizontal roadmap timeline
7 (Application) → ... → 1 (Physical)
7
Application
HTTP, FTP, DNS
6
Presentation
Encryption,
Compression
5
Session
★ MISSING
Dialogue
control
4
Transport
TCP/UDP,
Segments
3
Network
IP, Routing,
Packets
2
Data Link
★ MISSING
MAC,
Frames
1
Physical
Bits, Cables,
Signals
Why Session &amp; Data Link are essential
Session: manages dialogue &amp; resumes after interruption | Data Link: MAC framing + CRC error detection — together they complete the encapsulation chain end-to-end.
2

## Slide 3
Question 2
Data Units and Their OSI Layers
Each Protocol Data Unit (PDU) mapped to its OSI layer. Structure: diagonal card-stack (envelope wrapping)
Physical Layer | PDU: BITS
Electrical / optical / radio signals
Data Link Layer | PDU: FRAME
Adds MAC address + CRC trailer
Network Layer | PDU: PACKET
Adds source/destination IP
Transport Layer | PDU: SEGMENT
Adds ports + sequence numbers
Application Data | PDU: DATA
Innermost — original message
Physical
(outermost)
Data (innermost) →
Key idea
Each layer wraps the unit above it in its own header
Encapsulation: Data→Segment→Packet→Frame→Bits
Decapsulation un-wraps in reverse at the receiver
3

## Slide 4
Question 3
MAC Address vs IP Address in Data Delivery
Data Link → MAC Address → Local Delivery | Network → IP Address → Global Delivery | Structure: ladder comparison
MAC ADDRESS (Data Link Layer)
IP ADDRESS (Network Layer)
Local (same network segment)
Global (across networks)
Delivery Scope
Physical, burned into hardware
Logical, configurable
Nature
Yes — changes every hop
No — same end-to-end
Changes per hop?
Switches (within a LAN)
Routers (between networks)
Used by
Analysis
IP routes globally hop-by-hop; MAC delivers locally at each hop — a router re-encapsulates between the two for every hop along the path.
4

## Slide 5
Question 4
Error Control at Data Link vs Transport Layer
Error Control → Data Link → Error Detection | Error Control → Transport → Error Correction | Structure: swimlane process flow
Data Link Layer
Error Detection
Frame
arrives
CRC /
Checksum check
Corrupted →
drop frame
Transport Layer
Error Correction
Segment
sent
Timer / ACK
awaited
Lost →
retransmit
Analysis
Data Link acts locally, hop-by-hop and simply drops bad frames; Transport acts end-to-end and actively retransmits — a two-tier safety net.
5

## Slide 6
Question 5
Concept Map for Web Browsing Using OSI Layers
Request flows Layer 7→1 down, response flows 1→7 back up. Structure: circular loop
7
App
6
Pres.
5
Sess.
4
Trans.
3
Net.
2
D.Link
1
Phys.
Client
⇄ Server
Navy = request (down) | Coral = response (up)
If a layer fails:
• App: no page request possible
• Pres.: data unreadable/insecure
• Sess.: session breaks
• Trans.: data loss, page won't load
• Net.: site unreachable
• D.Link: local delivery corrupted
• Phys.: no connection at all
6

## Slide 7
Question 6
Troubleshooting Using the Concept Map
Given: Physical ✓ → Data Link ✓ → Network ✗ → Transport ✗ → Application ✗ | Structure: horizontal checklist ladder
1. Physical
✓ OK
Cable / Wi-Fi
confirmed working
2. Data Link
✓ OK
Local frames
delivered correctly
3. Network
✖ ROOT
IP/routing broken —
check gateway/subnet
4. Transport
✗ FAILS
No segments
delivered
5. Application
✗ FAILS
User sees
failure
Root-cause logic
Physical &amp; Data Link confirmed OK; Network is the first failing layer → root cause. Transport &amp; Application fail only as a downstream consequence — a bottom-up check narrows the fault fast.
7